## Slide 1: Road Building 101
General Road Construction Information

## Slide 2: Drainage: A Critical Factor
To account for surface water drainage, it is important that the road be constructed with a crown or cross slope. Typically, a crown is placed in the center of the road and the pavement is sloped 2% in each direction.
Drainage impacts pavement performance when the subgrade materials and pavement layer materials are saturated and loose strength. Water that falls on the pavement surface must be drained to curb and gutter systems or ditches. Water that penetrates the pavement from the surface; infiltrates from the sides of the road; or rises from under the pavement should not be allowed to compromise the overall strength.

## Slide 3: Key Road Building Components
Crown:
  The road surface should be higher in the center, not flat
Pitch:
  Road surface should be sloped 2 to 3 degrees lower from the center line to the edges
Base:
  The road surface should be supported by a strong base material, usually gravel
Shoulders:
  Each edge of the road should have a gravel shoulder
Ditches
  Wherever possible ditches should extend a short distance beyond each shoulder

## Slide 4: Basic Roadway Construction Diagram

## Slide 5: Typical Northwoods Chip Seal Cross Section
Chip Seal Surface
Gravel Base
Soil Type: Sand